## Slide 1: Personal Protective Equipment
An In-Service Training Program
Instructor Presentation & Notes
Provided Courtesy of
Notes: Source:
F880 – Infection Prevention and Control Program regulations and interpretive guidelines and CDC’s “Guidance for the Selection and Use of PPE in Healthcare Settings.”
Handouts: The following handouts are located in Part 2. Use at your discretion.
Handout #1 – Participant Session Outline.
Handout #2 – Sequence for Putting On PPE.
Handout #3 – Sequence for Removing PPE.
Handout #4 – Putting on and Taking off a Disposable Respirator.
Handout #5 – PPE Competency Validation Checklist.
Handout #6 – PPE Competency Evaluation Exam.
Modify this training session to meet your facility’s needs. Information is presented as a template only. Note: Be sure all participants sign the Record of Attendance form. (See Part 3)
OPTIONAL: Provide participants with a copy of Handout #1-Participant Session Outline.
Instructor Note: Keep in mind that during emergencies, PPE supplies may be limited. However, it is still crucial that your staff continue to follow the appropriate procedures for putting on and removing PPE. This training session addresses those issues and concerns.
CDC has released guidance on how to effectively use (OPTIMIZE) your supply of PPE when there is a shortage or limit on the availability of PPE. (See Part 3, beginning on page 5). Remember, these guidance documents do NOT eliminate the use of PPE, they only provide information on how to effectively use (optimize) your supply of PPE.
.

## Slide 2: Session Objectives
Upon completion of this training session, you should be able to:
Define personal protective equipment (PPE).
Discuss reasons PPE is NOT used.
Identify the types of PPE and their purpose.
Discuss three key factors to use when selecting PPE.
Discuss the process for selecting PPE.
Discuss key points about PPE.
Review the correct sequence of putting on and removing PPE.
Review and discuss scenarios concerning the selection of PPE.
Notes: Suggestion: Prior to moving to the next slide, ask participants how important the use of PPE is to them.
This will provide you with a sense of how knowledgeable your participants are about your facility’s use of personal protective equipment as well as their use of PPE.
Tell participants that each of these objectives are discussed during the training session.
Instructor Note: Remind participants that during emergencies, PPE supplies may be limited. However, it is still crucial that caregivers continue to follow the appropriate procedures for putting on, removing, and discarding PPE. This training session addresses those issues and concerns.
CDC has released guidance on how to effectively use (OPTIMIZE) your supply of PPE when there is a shortage or limit on the availability of PPE. (See Part 3, beginning on page 5). Remember, these guidance documents do NOT eliminate the use of PPE, they only provide information on how to effectively use (optimize) your supply of PPE.
.

## Slide 3: Definitions
Hand Hygiene is a general term that applies to hand washing with soap and water, or the use of a waterless alcohol-based antiseptic handrub (ABHR).
Personal Protective Equipment (PPE) is defined as protective items or garments worn by caregivers for protection against infectious materials and diseases, and to prevent cross-transmission of infectious materials and/or communicable diseases among residents.
Notes: Source: SOM Appendix PP, F880, Definitions.

## Slide 4: Reasons Staff Give for NOT Using Personal Protective Equipment (PPE)
It’s uncomfortable.
It doesn’t fit me.
Takes too long to put on and remove.
Interferes with my ability to do the task.
I forgot.
Not available when needed.
This task will only take a couple of minutes.
Too busy / not enough time.
Resident’s needs takes priority.
Notes: Suggestion: Before reviewing the reasons discussed here, ask participants to discuss reasons why they may not always use PPE when providing resident care.
Compare slide content with reasons participants gave.
Discuss as you deem necessary or appropriate to address the importance of using personal protective equipment (PPE).
If the availability of equipment and/or supplies is an issue, you should provide that information to Environmental Services, or other that has the authority to investigate and resolve such issues.
Other reasons you may want to discuss:
Culture.
Religious or health grounds.
Didn’t know about PPE.

## Slide 5: Types of PPE and their Purpose
Gloves – Protects the hands.
Gowns/Aprons – Protects the skin and/or clothing.
Masks – Protects the mouth and nose.
Respirators – Protects respiratory tract from airborne infectious agents.
Goggles – Protects the eyes.
Face Shields – Protects the face, mouth, nose, and eyes.
Notes: Inform participants that each of these items are discussed throughout this training session.
As you review each PPE item, ask participants if they have any concerns or issues about the use or purpose of the PPE item.
Instructor Note: It may be helpful to review and discuss CDC’s guidance documents for OPTIMIZING the supply of PPE before moving to the next slide. (See Part 3 – Support Documentation, beginning on page 5.)
Remind participants the these guidance documents do NOT eliminate how to put on, remove, or discard PPE. They only address how to OPTIMIZE their use when supplies are limited or exhausted.

## Slide 6: Factors Influencing PPE Selection
When selecting PPE, you should consider these three (3) things:
Type of Exposure Anticipated.
  Splash or Spray versus Touch.
  Category of Isolation Precautions.
Durability and Appropriateness for the Task.
Fit.
Notes: First is the type of anticipated exposure. This is determined by the type of anticipated exposure, such as touch, splashes or sprays, or large volumes of blood or body fluids that might penetrate the clothing. PPE selection, in particular the combination of PPE, is also determined by the category of isolation precautions a resident is on.
Second, and very much linked to the first, is the durability and appropriateness of the PPE for the task. This will affect, for example, whether a gown or apron is selected for PPE, or, if a gown is selected, whether it needs to be fluid resistant, fluid proof, or neither.
Third is fit. (optional question) How many of you have seen someone trying to work in PPE that is too small or large? PPE must fit the individual user. The facility provides PPE in sizes appropriate for individual caregivers. You should report PPE issues to your immediate supervisor or charge nurse.
(Segue to next slide) With the selection of PPE as background, let’s now discuss how to select and use specific PPE.

## Slide 7: Selecting Gloves
Gloves are the most common type of PPE used in healthcare settings. As you can see here, there are several things to consider when selecting the right glove for a specified purpose.
Purpose – resident care, environmental services, other.
Glove material – vinyl, latex, nitrile, other.
Sterile or nonsterile.
One or two pair.
Single use or reusable.
Notes: Most resident care activities require the use of a single pair of nonsterile gloves made of either latex, nitrile, or vinyl.
However, because of allergy concerns, some facilities have eliminated or limited latex products, including gloves, and now use gloves made of nitrile or other material. Vinyl gloves are also frequently available and work well if there is limited resident contact. However, some gloves do not provide a snug fit on the hand, especially around the wrist, and therefore should not be used if extensive contact is likely.
Gloves should fit the user’s hands comfortably – they should not be too loose or too tight. They also should not tear or damage easily. Gloves are sometimes worn for several hours and need to stand up to the task.
Who uses the other glove options? Sterile surgical gloves are worn by surgeons and other healthcare personnel who perform invasive resident procedures. During some surgical procedures, two pair of gloves may be worn.
Environmental services personnel often wear reusable heavy-duty gloves made of latex or nitrile to work with caustic disinfectants when cleaning environmental surfaces. However, they sometimes use the same types of gloves used in resident care.

## Slide 8: Use of Gloves
Gloving is necessary:
  When hands may become contaminated with blood, body fluids, excretions, or secretions, or when touching open wounds or mucous membranes, such as the mouth and respiratory tract.
  When touching items that are likely to be contaminated, such as urinary catheters and endotracheal tubes, and contaminated surfaces or objects.
  When resident care and the environment restrictions require it (e.g., isolation and contact precautions).
Notes: Ask participants to provide instances when they use gloves. Do they align with the points addressed here and/or with your facility’s policies?

## Slide 9: Do’s and Don’ts of Glove Use
Work from “clean to dirty.”
Limit opportunities for “touch contamination.” Protect yourself, others, and the environment:
  Don’t touch your face or adjust PPE with contaminated gloves.
  Don’t touch environmental surfaces except as necessary during resident care.
Change gloves:
  During use if torn and when heavily soiled (even during use on the same resident).
  After use on each resident.
Discard in appropriate receptacle:
  Never wash or reuse disposable gloves.
Notes: Gloves protect you against contact with infectious materials. However, once contaminated, gloves can become a means for spreading infectious materials to yourself, other residents or environmental surfaces. Therefore, the way YOU use gloves can influence the risk of disease transmission in your workplace. These are the most important do’s and don'ts of glove use:
Work from clean to dirty. This is a basic principle of infection control. In this instance it refers to touching clean body sites or surfaces before you touch dirty or heavily contaminated areas.
Limit opportunities for “touch contamination.” Protect yourself, others and environmental surfaces. How many times have you seen someone adjust their glasses, rub their nose or touch their face with gloves that have been in contact with a resident? This is one example of “touch contamination” that can potentially expose oneself to infectious agents. Think about environmental surfaces too and avoid unnecessarily touching them with contaminated gloves. Surfaces such as light switches, door and cabinet knobs can become contaminated if touched by soiled gloves.
Change gloves as needed. If gloves become torn or heavily soiled and additional resident care tasks must be performed, then change the gloves before starting the next task. Always change gloves after use on each resident and discard them in the nearest appropriate receptacle. Resident care gloves should never be washed and used again. Washing gloves does not necessarily make them safe for reuse; it may not be possible to eliminate all microorganisms and washing can make the gloves more prone to tearing or leaking.

## Slide 10: Selecting Gowns (or Aprons)
There are three (3) factors that influence the selection of a gown or apron as PPE.
Purpose of Use.
Material:
  Natural or man-made.
  Reusable or disposable.
  Resistance to fluid penetration.
Clean or Sterile.
Notes: First is the purpose of use. Isolation gowns are generally the preferred PPE for clothing, but aprons occasionally are used where limited contamination is anticipated. If contamination of the arms can be anticipated, a gown should be selected. Gowns should fully cover the torso, fit comfortably over the body, and have long sleeves that fit snuggly at the wrist.
Second are the material properties of the gown. Isolation gowns are made either of cotton or a spun synthetic material that dictate whether they can be laundered and reused or must be disposed. Cotton and spun synthetic isolation gowns vary in their degree of fluid resistance, another factor that must be considered in the selection of this garb. If fluid penetration is likely, a fluid resistant gown should be used.
The last factor concerns resident risks and whether a clean, rather than sterile gown, can be used. Clean gowns are generally used for isolation. Sterile gowns are only necessary for performing invasive procedures, such as inserting a central line.

## Slide 11: Selecting Face Protection
A combination of PPE types is available to protect all or parts of the face from contact with potentially infectious material. The selection of facial PPE is determined by the isolation precautions required for the resident and/or the nature of the resident contact.
Masks – protects the nose and mouth.
  Should fully cover the nose and mouth and prevent fluid penetration.
Goggles – protects the eyes.
  Should fit snuggly over and around the eyes.
  Personal glasses are NOT a substitute for goggles.
Face Shields – protects the face, nose, mouth, and eyes.
  Should cover the forehead, extend below chin and wrap around side of face.
Notes: Masks should fully cover the nose and mouth and prevent fluid penetration.
Masks should fit snuggly over the nose and mouth. For this reason, masks that have a flexible nose piece and can be secured to the head with string ties or elastic are preferable.
Goggles provide barrier protection for the eyes. Goggles should fit snuggly over and around the eyes or personal prescription lenses. Goggles with antifog features will help maintain clarity of vision
Personal prescription lenses do NOT provide optimal eye protection and should not be used as a substitute for goggles..
When skin protection, in addition to mouth, nose, and eye protection, is needed or desired, for example, when irrigating a wound or suctioning copious secretions, a face shield can be used as a substitute to wearing a mask or goggles.
The face shield should cover the forehead, extend below the chin, and wrap around the side of the face.

## Slide 12: Respiratory Protection
Purpose – protects from inhalation of infectious aerosols (e.g., Mycobacterium tuberculosis, COVID-19, etc.)
PPE types for respiratory protection:
  Particulate respirators.
  Half- or full-face elastomeric respirators.
  Powered air purifying respirators (PAPR).
Notes: PPE also is used to protect caregivers from hazardous or infectious aerosols, such as Mycobacterium tuberculosis, COVID-19, etc. Respirators that filter the air before it is inhaled should be used for respiratory protection.
The most commonly used respirators in healthcare settings are the N95, N99, or N100 particulate respirators.
Like other PPE, the selection of a respirator type must consider the nature of the exposure and risk involved. For example, N95 particulate respirators might be worn by personnel entering the room of a resident with tuberculosis or COVID-19.
Regardless of the respirator used, it is imperative that staff follow the manufacturer’s recommendations for use, fitting, and cleaning.
Instructor Note: Refer to the OSHA news release relative to the Temporary Enforcement Guidance for Respirator Fit-Testing located in Part 3, beginning on page 19.

## Slide 13: Key Points About PPE
KEY points to remember about PPE use:
Put on PPE before contact with the resident, generally before entering the room.
Use carefully – don’t spread contamination.
Remove and discard carefully, either at the doorway or immediately outside the resident’s room; remove respirator outside the room.
Immediately perform hand hygiene.
Notes: Put on PPE before you have any contact with the resident, generally before entering the room.
Once you have PPE on, use it carefully to prevent spreading contamination.
When you have completed your tasks, remove the PPE carefully and discard it in the receptacles provided.
Immediately perform hand hygiene before going on to the next resident.
Suggestion: Prior to moving to the next slide, select a participant to demonstrate the putting on and removing of PPE (e.g., gown, masks, goggles, gloves, etc.). Instruct the remaining participants to write down any incorrect procedures they may have observed.
Inform participants that the remaining session will be devoted to the proper sequence of putting on and removing PPE.
OPTIONAL: Provide participants with a copy of Handout #2 – Sequence for Putting On PPE.

## Slide 14: Putting On a Gown
Select appropriate type and size. Opening is in the back. Secure at neck and waist. If gown is too small, use two gowns. Gown #1 ties in front. Gown #2 ties in back. | 
Notes: To put on a gown, first select the appropriate type for the task and the right size for you.
The opening of the gown should be in the back; secure the gown at the neck and waist.
If the gown is too small to fully cover your torso, use two gowns.
Put on the first gown with the opening in front and the second gown over the first with the opening in the back.
OPTIONAL: Refer to Handout #2 – Sequence for Putting On PPE.

## Slide 15: Putting On a Mask
Place over nose, mouth, and chin. Fit flexible nose piece over the nose bridge. Secure on head with ties or elastic. Adjust to fit. | 
Notes: Some masks are fastened with ties, others with elastic.
If the mask has ties, place the mask over your mouth, nose and chin. Fit the flexible nose piece to the form of your nose bridge; tie the upper set at the back of your head and the lower set at the base of your neck.
If a mask has elastic head bands, separate the two bands, hold the mask in one hand and the bands in the other. Place and hold the mask over your nose, mouth, and chin, then stretch the bands over your head and secure them comfortably as shown; one band on the upper back of your head, the other below the ears at the base of the neck.
Adjust the mask to fit. Remember, you don’t want to be touching it during use so take the few seconds needed to make sure it is secure on your head and fits snuggly around your face so there are no gaps.
OPTIONAL: Refer to Handout #2 – Sequence for Putting On PPE.

## Slide 16: Putting On a Disposable Respirator
Position the respirator in your hands with the nose piece at your fingertips. Cup the respirator in hand allowing the headbands to hang below your hand. Hold the respirator under your chin with the nose piece up. The top strap goes over and rests at the top back of your head. The bottom strap is positioned around the neck and below the ear. Place your fingertips from both hands at the top of the metal nose clip (if present). Slide fingertips down both sides of the metal strip to mold the nose area to the shape of your nose. | 
Notes: Wash your hands thoroughly BEFORE putting on your respirator.
If you have used a respirator before that fits you, use the same make, model and size.
Inspect the respirator for damage. If your respirator appears damaged, DO NOT USE IT. Replace it with a new one.
Do not allow facial hair, hair, jewelry, glasses, clothing, or anything else to prevent proper placement or come between your face and the respirator.
Follow the instructions that come with your respirator.
OPTIONAL: Refer to Handout #4 – How to Properly Put on and Take off a Disposable Respirator.
Instructor Note: Refer to the OSHA news release relative to the Temporary Enforcement Guidance for Respirator Fit-Testing located in Part 3, beginning on page 19.

## Slide 17: Checking Your Seal on a Disposable Respirator
Place both hands over the respirator. Take a quick BREATH IN to check whether the respirator seals tightly to the face. Place both hands completely over the respirator and EXHALE. If you feel leakage, there is NOT a proper seal. If air leaks around the nose, re-adjust the nose piece. If air leaks at the mask edges, re-adjust the straps along the sides of your head until a proper seal is achieved. If you cannot achieve a proper seal due to air leakage, notify your supervisor. A different size or model may be necessary. | 
Notes: Wash your hands thoroughly BEFORE putting on your respirator.
If you have used a respirator before that fits you, use the same make, model and size.
Inspect the respirator for damage. If your respirator appears damaged, DO NOT USE IT. Replace it with a new one.
Do not allow facial hair, hair, jewelry, glasses, clothing, or anything else to prevent proper placement or come between your face and the respirator.
Follow the instructions that come with your respirator.
OPTIONAL: Refer to Handout #4 – How to Properly Put on and Take off a Disposable Respirator.
Instructor Note: Refer to the OSHA news release relative to the Temporary Enforcement Guidance for Respirator Fit-Testing located in Part 3, beginning on page 19.

## Slide 18: Putting On Eye and Face Protection
Position goggles over eyes and secure to the head using the ear-pieces or headband. Position face shield over face and secure on brow with headband. Adjust to fit comfortably. | 
Notes: If eye protection is needed, either goggles or a face shield should be worn.
Position either device over the face and/or eyes and secure to head using the attached ear-pieces or head band.
Adjust to fit comfortably. Goggles should feel snug but not tight.
OPTIONAL: Refer to Handout #2 – Sequence for Putting On PPE.

## Slide 19: Putting On Gloves
Put on your gloves last. Select correct type and size. Insert hands into gloves. Extend gloves over isolation gown cuff. | 
Notes: The last item of PPE to be put on (donned) is a pair of gloves.
Be sure to select the type of glove needed for the task in the size that best fits you. Insert each hand into the appropriate glove and adjust as needed for comfort and dexterity.
If you are wearing an isolation gown, tuck the gown cuffs securely under each glove. This provides a continuous barrier protection for your skin.
OPTIONAL: Refer to Handout #2 – Sequence for Putting On PPE.

## Slide 20: How to Safely Use PPE
Keep gloved hands away from face.
Avoid touching or adjusting other PPE.
Remove gloves if they become torn; perform hand hygiene before putting on new gloves.
Limit surfaces and items touched.
Notes: In addition to wearing PPE, you should also use safe work practices.
Avoid contaminating yourself by keeping your hands away from your face and not touching or adjusting PPE.
Also, remove your gloves if they become torn and perform hand hygiene before putting on a new pair of gloves.
You should also avoid spreading contamination by limiting surfaces and items touched with contaminated gloves.
OPTIONAL: Refer to Handout #2 – Sequence for Putting On PPE. See “Safe Practices” at bottom of page.

## Slide 21: “Contaminated” and “Clean” Areas of PPE
To remove PPE safely, you must first be able to identify what sites are considered “clean” and what are “contaminated.”
Contaminated – outside front:
  Areas of PPE that have or are likely to have been in contact with body sites, materials, or environmental surfaces where the infectious organism may reside.
Clean – inside, outside back, ties on head and back:
  Areas of PPE that are not likely to have been in contact with the infectious organism.
Notes: In general, the outside front and sleeves of the isolation gown and outside front of the goggles, mask, respirator and face shield are considered “contaminated,” regardless of whether there is visible soil. Also, the outside of the gloves are contaminated.
The areas that are considered “clean” are the parts that will be touched when removing PPE. These include:
inside the gloves;
inside and back of the gown, including the ties;
and the ties, elastic, or ear-pieces of the mask, goggles and face shield.
Instructor Note: Tell your participants that during the next several slides you will be discussing important information on HOW to REMOVE personal protective equipment (PPE).
OPTIONAL: Provide participants with Handout #3 – Sequence for Removing PPE.

## Slide 22: Sequence for Removing PPE
The sequence for removing PPE is intended to limit opportunities for self-contamination. Remove PPE in the following sequence:
Gloves.
Face Shield or Goggles.
Gown.
Mask or Respirator.
Notes: The gloves are considered the most contaminated pieces of PPE and are therefore removed first.
The face shield or goggles are next because they are more cumbersome and would interfere with removal of other PPE.
The gown is third in the sequence, followed by the mask or respirator.
OPTIONAL: Refer to Handout #3 – Sequence for Removing PPE.

## Slide 23: Where to Remove PPE
At doorway, before leaving the resident room or in the anteroom.
Remove respirator outside room, after door has been closed.
Be sure that hand hygiene facilities and trash receptacles are available at the point needed, e.g., sink or alcohol-based hand rub.
Notes: If only gloves are worn as PPE, it is safe to remove and discard them in the resident’s room. Place in designated receptacle.
When a gown or full PPE is worn, PPE should be removed at the doorway or in an anteroom.
Respirators should always be removed outside the resident’s room, after the door is closed.
Hand hygiene should be performed after all PPE is removed.
OPTIONAL: Refer to Handout #3 – Sequence for Removing PPE.

## Slide 24: Removing the 1st Glove
Grasp OUTSIDE edge near the wrist.
Peel AWAY from hand, turning glove
inside-out.
Hold in opposite gloved hand.
Notes: Using one gloved hand, grasp the outside of the opposite glove near the wrist.
Pull and peel the glove away from the hand.
The glove should now be turned inside-out, with the contaminated side now on the inside.
Hold the removed glove in the opposite gloved hand.
OPTIONAL: Refer to Handout #3 – Sequence for Removing PPE.

## Slide 25: Removing the 2nd Glove
Slide UNGLOVED finger under the wrist
of the remaining glove.
Peel AWAY from inside, creating a bag
for both gloves.
Discard in appropriate waste receptacle.
Notes: Slide one or two fingers of the ungloved hand under the wrist of the remaining glove.
Peel glove off from the inside, creating a bag for both gloves.
Discard in appropriate waste receptacle.
OPTIONAL: Refer to Handout #3 – Sequence for Removing PPE.

## Slide 26: Removing Goggles or Face Shield
Grasp ear or head pieces with your ungloved
hands.
Lift AWAY from your face.
Place in designated receptacle for
reprocessing or disposal.
Notes: Using ungloved hands, grasp the “clean” ear or head pieces and lift away from face.
If goggle or face shield are reusable, place them in a designated receptacle for subsequent reprocessing. Otherwise, discard them in the waste receptacle.
OPTIONAL: Refer to Handout #3 – Sequence for Removing PPE.

## Slide 27: Removing the Isolation Gown
Unfasten ties.
Peel gown AWAY from the neck
and shoulder.
Turn contaminated OUTSIDE toward
the INSIDE.
Fold or roll into a bundle.
Discard in appropriate waste receptacle.
Notes: Unfasten the gown ties with the ungloved hands.
Slip hands underneath the gown at the neck and shoulder, peel away from the shoulders.
Slip the fingers of one hand under the cuff of the opposite arm. Pull the hand into the sleeve, grasping the gown from inside.
Reach across and push the sleeve off the opposite arm.
Fold the gown towards the inside and fold or roll into a bundle. (Only the “clean” part of the gown should be visible.)
Discard into waste or linen container, as appropriate.
OPTIONAL: Refer to Handout #3 – Sequence for Removing PPE.

## Slide 28: Removing a Mask
Untie the bottom string, then the top string.
If elastic bands, remove the bottom band first
then remove the top band.
Remove from the face.
Do NOT touch the front of the mask as it
is considered contaminated.
Discard in appropriate waste receptacle.
Notes: The front of the mask is considered contaminated and should not be touched.
Remove by handling only the ties or elastic bands starting with the bottom then top tie or band.
Lift the mask away from the face and discard it into the designated waste receptacle.
OPTIONAL: Refer to Handout #3 – Sequence for Removing PPE.

## Slide 29: Removing a Particulate Respirator
Do NOT touch the front of the mask as it
is considered contaminated.
Lift the BOTTOM elastic over your head first.
Then LIFT off the TOP elastic.
Discard in appropriate waste receptacle.
Notes: The bottom elastic should first be lifted over the head. Then remove the top elastic.
This should be done slowly to prevent the respirator from “snapping” off the face.
Do NOT touch the front of the mask as it is considered contaminated.
Remove the Respirator Mask outside the resident’s room, after the door is closed.
Wash your hands.
OPTIONAL: Refer to Handout #4 – How to Properly Put On and Take Off a Disposable Respirator.
Instructor Note: Refer to the OSHA news release relative to the Temporary Enforcement Guidance for Respirator Fit-Testing located in Part 3, beginning on page 19.

## Slide 30: Hand Hygiene
Perform hand hygiene immediately after removing PPE.
  If hands become visibly contaminated during PPE removal, wash hands before continuing to remove PPE.
Wash hands with soap and water or use an alcohol-based hand rub.
Ensure that hand hygiene facilities are available at the point needed, e.g., sink or alcohol-based hand rub.
Notes: Hand hygiene is the cornerstone of preventing infection transmission.
You should perform hand hygiene immediately after removing PPE.
If your hands become visibly contaminated during PPE removal, wash hands before continuing to remove PPE.
Wash your hands thoroughly with soap and warm water or, if hands are not visibly contaminated, use an alcohol-based hand rub.
Instructor Note: Tell participants that you will now review some instances that require the use of PPE and participants will be asked to discuss which PPE they would select for each scenario and why.

## Slide 31: What Type of PPE Would YOU Wear in These Scenarios?
Giving a bed bath?
Suctioning oral secretions?
Transporting a resident in a wheel-chair?
Responding to an emergency where blood is spurting?
Drawing blood from a vein?
Cleaning an incontinent resident with diarrhea?
Irrigating a wound?
Taking vital signs?
Notes: Listed here are several resident care activities that could indicate a need to wear PPE. What PPE would YOU wear for the following?
Giving a bed bath? (generally none).
Suctioning oral secretions? (gloves and mask/goggles or a face shield) (Respondents may correctly note that this may depend on whether open or closed suction is being used).
Transporting a resident in a wheelchair? (generally none).
Responding to an emergency where blood is spurting? (gloves, fluid-resistant gown, mask/goggles or a face shield).
Drawing blood from a vein? (gloves).
Cleaning an incontinent resident with diarrhea? (gloves and generally a gown).
Irrigating a wound? (gloves, gown, and mask/goggles or a face shield).
Taking vital signs? (generally none).
Instructor Note: Encourage discussion of how caregivers decide for themselves which PPE will be worn. Do they over- or under-protect themselves?. Discuss responses as appropriate to ensure participants understand the importance of the use of PPE.

## Slide 32
Question and Answer Session
Notes: Encourage participants to ask questions to ensure they have a working understanding of how and when to use personal protective equipment (PPE).
OPTIONAL: Using Handout #5, conduct a Personal Protective Equipment (PPE) Competency Validation Checklist for each participant to determine if they can successfully demonstrate the putting on, taking off, and disposal of PPE.
Using Handout #6, conduct a Competency Evaluation Exam for each participants to determine their knowledge and competency level concerning the use of PPE. (See below for Exam Answer Key)
Using the results of the Validation Checklist and the Competency Evaluation Exam, modify your Personal Protective Equipment (PPE) training program as necessary to address any identified issues or concerns.
Instructor Note: Remind participants to sign the Record of Attendance Form. Be sure to complete recordkeeping documentation. (See Part 3)
Exam Answer Key and Slide Location Where the Answer can be Found:
1=T (Slide #6); 2=T (Slide #9); 3=T (Slide #10); 4=F (Slide #11); 5=F (Slide #13); 6=F (Slide #14); 7=T (Slide #17); 8=F (Slide #19); 9=T (Slide #20); 10=F (Slides #22); 11=T (Slide #23); 12=F (Slide #23); 13=T (Slide #29); 14=F (Slide #30); 15=T (Slide #30)